## Slide 1
GPU ↔ WSE-3: one speculative-decoding round-trip
Verifier idle the whole 3.30 ms; wafer compute only 0.166 ms (5%). Batched d2h receive is the win: 6.2 → 3.30 ms (~1.9×).
GPU verify target model
draft frontend gateway + worker
WSE-3 wafer draft kernel
DraftAdvanceCommand — commit + next_proposal (k=16)
h2d send — run draft command
draft kernel emits sampled token(s)
batch d2h — 1 receive
DraftAdvanceResult — proposal.draft_ids[16]
round-trip timing · p50
verify-side (GPU ↔ WSE): 3.30 ms
driver-side (frontend ↔ WSE): 1.93 ms
wafer compute: 0.166 ms (5%)

## Slide 2
Protocol: the gRPC stream
One long-lived bidi stream. GPU verify_service = server; WSE draft_service = client.
service DraftControl → rpc OpenStream( stream DraftServiceMessage ) returns ( stream VerifyServiceMessage )
verify → draft (GPU → WSE)
DraftAdvanceCommand
per-round work — the request
Ping
keepalive
draft → verify (WSE → GPU)
DraftServiceHello
register on stream open
DraftAdvanceResult
per-round reply
Pong
keepalive

## Slide 3
Protocol: the request
DraftAdvanceRequest — sent verify → draft each round.
DraftAdvanceRequest
request_id correlation id
expected_version concurrency guard
expected_len committed-length guard
commit (DraftCommit) verdict on previous round
next_proposal (NextProposal) request k drafts
DraftCommit
round_id · base_version · base_len
accepted_draft_tokens # accepted
emitted_ids committed tokens
NextProposal
round_id requested round
k # draft tokens (= draft_len)

## Slide 4
Protocol: the response
DraftAdvanceResponse — returned draft → verify each round.
DraftAdvanceResponse
request_id echoes request
committed_version version after commit
committed_len length after commit
commit_result (CommitResult) what was applied
Proposal (Proposal) freshly drafted tokens
status READY | PROPOSAL_PENDING
CommitResult
round_id committed round
old/new version · len before / after
accepted_draft_tokens # accepted
Proposal
round_id · base_version · base_len
draft_ids candidate tokens
draft_len = k

## Slide 5
The gateway ↔ kernel wire frame
The compact u32 frame below the gRPC service boundary. Leg (1) gRPC is unchanged.
FORWARD gateway → kernel
u32 ingress · zero-padded to in_wlts = 19
request[] = [ flags, num_accepted, num_correction, correction_ids ]
flags HAS_COMMIT · HAS_PROPOSAL · PREFILL
num_accepted drafts kept from last round
num_correction = len(correction_ids)
correction_ids = emitted_ids[num_accepted:]
k rides beside the frame (0 | draft_len) — not piped to the kernel
BACKWARD kernel → gateway
u32 egress
reply[] = [ draft_id_0, … draft_id_{k-1} ] · k = draft_len (16)
south-blobs draft_len × south_wlts u32
sampled slot = sampled_off
exchange_batch [ blob[i*sw + off] ]
decode → Proposal.draft_ids
passthrough kernel echoes today; a real decode kernel acts on it
committed_len / base_len stay off the wire — recovered by accumulation (num_accepted + num_correction), SGLang-style kv_committed_len.

## Slide 6
One protocol, two kernels
The fork is in the executor, not the wire — leg 1 gRPC never changes.
gRPC request DraftAdvanceRequest token-ids — identical for both
DECODE kernel embed-a-token · keep KV, ingest 1, draft k
PREFILL kernel ingest-raw-ids · embed N, build KV[0:N], sample
shared egress south blob — same layout for both
Same request on the wire; the divergence lives below the service boundary, in the executor adapter and kernels.

## Slide 7
Decode vs prefill: wafer ingress (leg 2)
Same protocol, two ingress paths — and what prefill still needs.
 | DECODE (real qwen3_1p7b) | PREFILL (to finalize)
gRPC call | commit{accepted=N} + next_proposal{k} | commit{accepted=0, emitted=prompt}
wafer ingress | f16 embeddings · bsz*dim/2 u32 | i32 token ids · ~bsz*seq_len u32
tokens / call | 1 (the correction) | N (the whole prompt)
kernel action | keep KV, ingest 1, draft k | parallel-embed N, build KV[0:N]
egress (south blob) | val_wlts + top_k*bsz + bsz | SAME layout (×1)
Prefill ingress should be: [ num_tokens, tok_0, … tok_{n-1} ] (i32)
num_tokens is the length header prefill lacks today (currently fixed by MAX_SEQ_LEN).
Minimal change: gRPC (leg 1) unchanged · prefill kernel adds a num_tokens header · path chosen by appliance routing, not a wire flag.